## Slide 1: Chapter 10: Link Layer
CS433 เครือข่ายคอมพิวเตอร์

## Slide 2: Outline
Introduction
Error Detection, Correction
Multiple Access Protocols
LANs
Link Virtualization: MPLS
Data Center Networking

## Slide 3: Terminology
Nodes: Hosts, Routers
Links: Wired Links, Wireless Links
Frame: Layer-2 Packets (Encapsulate Datagrams)

## Slide 4: Link Layer
Datagram travel over different links
  e.g. sent from 802.11 (Wireless) to AP, AP send to its intermediate links on Ethernet, then send out using Frame Relay
Each link protocol may provide different services
  e.g. Some may not provide RDT

## Slide 5: Link Layer Services
Transferring Datagram from one node to physically adjacent node
Framing Datagram
Link Access: Medium Access Control (MAC)
Reliable Delivery between adjacent nodes: RDT, use on wireless links

## Slide 6: Link Layer Services
Flow Control
  Pacing control between adjacent sending and receiving nodes
Error Detection
  Error from noise, signal attenuation then drop error frame
Error Correction
  Receivers correct bit errors without retransmission
Half-duplex vs Full-duplex
  nodes at both ends can transmit but not at the same time

## Slide 7: Link Layer Implementation
In each host
In adaptor (NIC) or network chip
  Ethernet card, 802.11 card
Attaches into host’s system buses
Combination of hardware, software, firmware

## Slide 8: Adaptors Communicating
Sender
  Encapsulate datagram
  RDT, flow control
Receiver
  Error checking, RDT, flow control
  Decapsulate
    Pass datagram to upper layer
Sender
Receiver

## Slide 9: Outline
Introduction
Error Detection, Correction
Multiple Access Protocols
LANs
Link Virtualization: MPLS
Data Center Networking

## Slide 10: Error Detection
D: Data
EDC: Error Detection and Correction bits
*Error detection not 100% reliable
**Larger EDC = better detection

## Slide 11: Parity Checking
Single bit parity
Two-dimensional
bit parity
Detect and correct single bit errors

## Slide 12: Internet Checksum
Transport Layer Checksum
  Checksum of the whole segment (header+data)
Network Layer Checksum
  Checksum of the IP header only
Link Layer Checksum?
  Cyclic Redundancy Check (CRC)

## Slide 13: Cyclic Redundancy Check (CRC)
More powerful than checksum
Widely used in practice (Ethernet, 802.11, ATM)
Given D as data, G as generator and R is CRC-bits
<D, R> divide by G (mod 2), if the result has non-zero bit => Error
D: Data bits to be sent
R: CRC bits
d bits
r bits

## Slide 14: CRC Example
D = 101110000
G = 1001
R = = 011
ถ้าขนาดของ CRC มี n ตัว
ให้เติม 0 เป็นจำนวน n ตัวหลังข้อมูลที่ต้องการจะหาค่า CRC
XOR กัน

## Slide 15: Outline
Introduction
Error Detection, Correction
Multiple Access Protocols
LANs
Link Virtualization: MPLS
Data Center Networking

## Slide 16: Multiple access links
Two types of links
Point-to-point (PPP)
  PPP for dial-up access
  Point-to-point links between Ethernet switch and host
Broadcast
  Ethernet hub
  802.11 WiFi

## Slide 17: Multiple Access Protocols
Single shared broadcast channel
Two or more simultaneous transmission
  Interference (Collision) -> Error
Multiple access protocol: algorithm determines how nodes share channel
No additional channel for coordination

## Slide 18: Ideal Multiple Access Protocol
Given channel of rate R bps
  Only 1 node transmit, the node can transmit at rate R
  M nodes transmit, each node can transmit at rate R/M
  Decentralized: no manager node, no clock synchronization
  Simple

## Slide 19: Class of MAC Protocols
Channel Partitioning
  divide channel into smaller slot (e.g. time slot, frequency)
  then allocate each slot to node
Random Access
  Allow collisions
  Then recover from collisions
Taking turns
  Nodes take turns
  node with more to send taking longer turns

## Slide 20: Channel Partitioning - TDMA
Time Division Multiple Access (TDMA)
  hosts get fixed length slot to send (Packet transmission time)
  Unused slot go idle (wasted bandwidth)
  Example: 4 slot TDMA, and host 1, 3, 4 sending
1
3
4
4 slot frame
Time
1
3
4
4 slot frame
1
3
4
4 slot frame

## Slide 21: Channel Partitioning - FDMA
Frequency Division Multiple Access (FDMA)
  hosts get their own fixed frequency bands

## Slide 22: Random Access Protocols
If you want to send, just send
But if two or more nodes transmitting at the same time -> Collision
Random Access Protocol:
  detect collisions
  recover from collisions (e.g. delayed retransmission)
Example protocols
  Slotted ALOHA, ALOHA
  CSMA, CSMA/CD, CSMA/CA

## Slide 23: ALOHA
No slot, fully decentralized

## Slide 24: Slotted ALOHA
All frames same size
Time divided into equal size slots
Nodes start to transmit only slot beginning
Nodes are synchronized
2 or more transmit at the same slot (same time), all node detect collision

## Slide 25: Slotted ALOHA

## Slide 26: Slotted ALOHA
When nodes obtains new frame, transmits in next slot
  If no collision: node sends new frame in next slot
  If collision: node retransmits frame in each subsequent slot with probability p until success

## Slide 27: Carrier Sense Multiple Access (CSMA)
Listen before transmission
  If channel is idle, transmit the full packet
  If not idle, wait
Collision still occur
  At the time or listening, channel is idle, but because of the propagation delay, node may not hear
  distance, propagation delay

## Slide 28: CSMA/CD
Collision Detection (CD)
  Once notice collision, stop transmission
  In Wired: detect by signal strength compare with transmission power

## Slide 29: Ethernet CSMA/CD
NIC received datagram from Network Layer
If NIC senses channel idle, start frame transmission,
or if NIC senses channel is busy, delay the transmission.
If NIC transmits frame without detecting collision, job done.
4. but if NIC detects collision, aborts the transmission and send jam signal
After aborting, NIC enter binary (exponential) backoff
  Mth collision, NIC chooses K at random from {0,1,2, …, 2m-1} and wait for K x 512 bit times, then goes back to Step 2
More Collision = Longer Backoff

## Slide 30: Taking Turns
Channel Partitioning
  High load -> Efficient
  Low load -> Inefficient, delay in channel access 1/N bandwidth
Random Access
  Low load -> Efficient
  High load -> Collision overheads
Taking turns?

## Slide 31: Polling protocol: Taking turns
Having Master node and Slave nodes
Master node invites slave to transmit in turn
Concerns: polling overheads, latency, single point of failure (at master node)
Practical use in Bluetooth
Poll
Data
Data
Data
Master node
Slave node
Slave node
Slave node

## Slide 32: Token passing: Taking turns
Token: node, which controls token, can transmit upto n datagrams then pass the token message to the next node.
Token message will be passed in order manner
Concerns: Token overheads, latency and token lost? What to do?
Data
Data
Data
Data
Token

## Slide 33: Summary of MAC
Channel Partitioning
  Time Division, Frequency Division
Random Access
  ALOHA, S-ALOHA
  CSMA/CD (Ethernet), CSMA/CA (802.11)
Taking Turns
  Polling, Token Ring

## Slide 34: Outline
Introduction
Error Detection, Correction
Multiple Access Protocols
LANs
Link Virtualization: MPLS
Data Center Networking

## Slide 35: LANs
Addressing
ARP
MAC
Ethernet
Switches
VLANs

## Slide 36: Addressing
IP address 32bit
  Network layer address for interface
  Used for Network Layer (Layer 3) forwarding
MAC address (Physical address)
  Used to get frame from one interface to another physically-connected interface (in the same IP network)
  48 bit MAC address burned in to NIC ROM
  e.g. 1A-2F-BB-76-09-AD (in hex code - 4bit each)

## Slide 37: MAC Address
Each NIC has unique MAC address
Links can be either
wired or wireless

## Slide 38: MAC addresses
MAC addresses (Physical or LAN address) are allocated by IEEE
Manufacturer buys portion of MAC address
Analogy:
  MAC address: national ID
  IP: postal address

## Slide 39: ARP: Address Resolution Protocol
mapping: MAC address and IP address.
ARP table contains each pair of IP and MAC addresses for each node along with TTL
TTL: Time to live is a time after address will be forgotten. Typically remember for 20 mins
IP Address | MAC Address | TTL
192.168.1.15 | 1A:2D:3C:FF:AB:3D | 17:50:10
192.168.1.55 | 3D:4F:AA:20:1C:40 | 09:14:02
ARP Table

## Slide 40: ARP Protocols
A wants to send datagram to B
  A’s ARP table doesn’t have B’s MAC address
A broadcast ARP query packet, containing B’s IP
B receives ARP query, then reply A with its MAC
A receives B’s MAC address then save into its ARP table.
ARP is “Plug-and-play”, nodes create their ARP table when join networks themselves
***When nodes join network, nodes get IP using DHCP, then use ARP to get MAC***

## Slide 41: Sending Datagram from A to B
Assume A got B’s IP address
How A knows R’IP and R’s MAC address?
Node A
Node B
Router R

## Slide 42: Sending datagram A to B
A create IP datagram with IP Src of A, IP Dst of B
Create Link Layer frame with R’s MAC as Dst
Node A
Node B
Router R
MAC Src: 74-29-9C-E8-FF-55
MAC Dst: E6-E9-00-17-BB-4B
IP Src: 111.111.111.111
IP Dst: 222.222.222.221
Segment

## Slide 43: Sending datagram A to B
Frame sent from A to R
R received the frame, remove link layer header, pass it up to network layer
Node A
Node B
Router R
MAC Src: 74-29-9C-E8-FF-55
MAC Dst: E6-E9-00-17-BB-4B
IP Src: 111.111.111.111
IP Dst: 222.222.222.221
Segment

## Slide 44: Sending datagram A to B
R forwards datagram with IP src A, dst B
R create link layer frame with B’s MAC as dst
Node A
Node B
Router R
MAC Src: 1A-23-F9-CD-06-9B
MAC Dst: 88-B2-2F-54-1A-0F
IP Src: 111.111.111.111
IP Dst: 222.222.222.221
Segment

## Slide 45: Sending datagram A to B
R forwards datagram with IP src A, dst B
R create link layer frame with B’s MAC as dst
Node A
Node B
Router R
MAC Src: 1A-23-F9-CD-06-9B
MAC Dst: 88-B2-2F-54-1A-0F
IP Src: 111.111.111.111
IP Dst: 222.222.222.221
Segment

## Slide 46: Chapter 10 Summary
Link Layer Introduction
Error Detection, Correction: Checksum, CRC
MAC: ALOHA, CSMA/CD
LAN: Addressing, ARP

## Slide 47: ARP Spoofing
A
B
C
Switch
Router/Gateway
Internet
C->Broadcast
ใครมี MAC address
ชอง Gateway R1 มั่ง
(2) R1->C
MAC Address ของ R1 คือ
AB:CD:01:02:…
(3) C อัพเดต ARP table

## Slide 48: ARP Spoofing
A
B
C
Attacker
M
Switch
Router/Gateway
Internet
C->Broadcast
ใครมี MAC address
ชอง Gateway R1 มั่ง
(2) M->C
MAC Address ของ R1 คือ
00:00:00:00:… (ปลอมขึ้นมา)
(3) C อัพเดต ARP table
ด้วยข้อมูลผิดๆ